Progress in Optical Access  Standards
Joint ITU/IEEE Workshop on Ethernet - Emerging Applications and Technologies
(Geneva, Switzerland, 22 September2012)
Progress in Optical Access
Standards
Frank Effenberger
Rapporteur Q2/15
VP Access R&D, Futurewei

---
Agenda – PON Evolution
Agenda – PON Evolution
- G-PON
- NG-PON1 = XG-PON
- NG-PON2 = TWDM-PON
- Other topics

---
Capacity Trend for PON
Capacity Trend for PON
250G
Bandwidth
250G
100G
100G
40G
40G
40G
Downstream
Upstream
10G
10G
2.5G
0.6G
0.15G
0.05G
Generation
1994
TPON
1999
A-PON
B-PON
2004
G-PON
GEPON
2009
NG-PON1
XG-PON
10GEPON
2014
NG-PON2
TWDM-PON
2020+
NG-PON3
?

---
G-PON: Widely deployed
G-PON: Widely deployed
System defined in the G.984 series
  - G.984.1: System requirements
  - G.984.2: PMD specifications
  - G.984.3: TC specifications
  - G.984.4: OMCI - Subsumed by G.988
    - Now used for all ITU PONs and P2P systems
  - G.984.5: WDM matters for the future
  - G.984.6: Reach extension
  - G.984.7: Long reach
  - Plus supplements…
- Standards considered stable and mature
- Minor optional enhancements continue even now

---
XG-PON1 system (G.987 series)  coexisting with G-PON
XG-PON1 system (G.987 series)
coexisting with G-PON
GPON OLT
GPON ONU
GPON
OLT
MAC
Logic
OLT Tx
1490nm
ONU Rx
1490nm
GPON
ONU
MAC
Logic
NNI
Data
I/O
UNI
Data
I/O
1490nm
WDM
WDM
OLT Rx
1310nm
ONU Tx
1310nm
1577nm
WDM1
XG-PON OLT
XG-PON ONU
1310nm
XGPON
OLT
MAC
Logic
OLT Tx
1577nm
ONU Rx
1577nm
XGPON
ONU
MAC
Logic
NNI
Data
I/O
UNI
Data
I/O
1270nm
WDM
WDM
OLT Rx
1270nm
ONU Tx
1270nm

---
XG-PON1 PMD specifications:  G.987.2
XG-PON1 PMD specifications:
G.987.2
- Six OLT types and two ONU types
- Four loss budgets in all
N1 OLT
Tx: +2 ~ +6
Rx: -7 ~ -27.5
N2a OLT
Tx: +4 ~ +8
Rx: -9 ~ -29.5
E1 OLT
Tx: +6 ~ +10
Rx: -11 ~ -31.5
E2a OLT
Tx: +8 ~ +12
Rx: -11 ~ -31.5
N2b OLT
Tx: +10.5 ~ +12.5
Rx: -9 ~ -29.5
E2b OLT
Tx: +14.5 ~ +16.5
Rx: -13 ~ -33.5
29dB
31dB
33dB
35dB
31dB
35dB
APD ONU
Tx: +2 ~ +7
Rx: -8 ~ -28
PIN ONU
Tx: +2 ~ +7
Rx: -3.5 ~ -22.5

---
XG-PON TC layer structure : G.987.3
XG-PON TC layer structure :
G.987.3
The XG-PON TC layer is broken into 3 layers
  - Simplified implementation
  - Improved extensibility
Service adaptation Sublayer
Encapsulated users data
Interfaces with Framing layer
Framing Sublayer
Implements essential TDMA
Control and signaling
PHY adaptation Sublayer
Encapsulates frame and
Interfaces with PHY layer

---
First XG-PON trial in the world
First XG-PON trial in the world
March 2010

---
NG-PON2: Technology Map
NG-PON2: Technology Map
64
DWDM
PON
OFDM
PON
16
2
3
TWDM
PON
4
4
1
A-
PON
B-
PON
G-
PON
XG-
PON
XLG-
PON
1
155M
622M
2.5G
10G
40G
Bit Rate
Number of Wavelengths
UDWDM
PON

---
1. XLG-PON 40G/10G TDM PON
1. XLG-PON 40G/10G TDM PON
10G APD BMR
re-use 10G EPON PR-30
Add BM EDC to gain 2 dB
40 km reach
40 km diff. distance
31 dB loss budget
ONU
OLT
10G US
EDC
BM APD Rx
40G DS
1:N
EML
SOA
40G integrated EML + SOA
Integration driven by XG-PON N2b
40G duobinary modulation (electrical)
+10 dBm output
APD Rx
Bit-interleaving protocol
Dynamic bandwidth
User-rate ONU electronics
20 GHz APD Rx
Duobinary demodulation (electrical)
Efficient FEC (e.g. LDPC)
-22 dBm sensitivity
Logic
Logic

---
2. WDM mux-based WDM PONs: Passive Photonic Loop
2. WDM mux-based WDM PONs:
Passive Photonic Loop
ONU1
Xcvr1
ONU2
Xcvr2
Xcvr3
WDM
MUX
WDM
MUX
ONU3
Colorless ONU type 1
ONU receives only one downstream wavelength
ONU must transmit on the correct upstream wavelength

---
2A-C. Wavelength Injection types
2A-C. Wavelength Injection types
2A. External Injection
2B. Wavelength Reuse
2C. Self Seeded
ONU
IL FP
Rx
Logic
OLT
Rx
DFB Tx
Logic
ASE
Seed
Tx/Rx
Tx/Rx
AWG
ONU
RSOA
Rx
Logic
AWG
1535
1560
ASE light
1535
1560
ASE slice
1535
1560
After locking
1535
1560
Before locking
Reflective
Gain
zone
1535
1560
ASE slice in
1535
1560
Amplified light out
RSOA
ONU
RSOA
Rx
Logic
OLT
Rx
DFB Tx
Logic
Tx/Rx
Tx/Rx
AWG
AWG
Power
Splitter
EYE Distortion
Reflective
Gain
zone
1535
1560
Rx λ in
1535
1560
Amplified λ out
RSOA
0
0
0
1
1
1
Rx data modulation
ONU
IL FP
Rx
Logic
OLT
Rx
RSOA
Logic
Tx/Rx
Tx/Rx
AWG
ONU
RSOA
Rx
Logic
AWG
1535
1560
After locking
1535
1560
Before locking
Reflective
Gain
zone
RSOA
1535
1560
ASE slice in
1535
1560
Amplified light out
1535
1560
ASE light
FRM
FRM

---
2. Splitter-based WDM PONs: Lambda Net
2. Splitter-based WDM PONs: Lambda Net
ONU1
Splitter
Xcvr1
ONU2
Xcvr2
Xcvr3
WDM
MUX
ONU3
Colorless ONU type 2
ONU must tune to the correct downstream wavelength
ONU must transmit on the correct upstream wavelength

---
2D-E. Tunable ONUs
2D-E. Tunable ONUs
2D. Conventional tuned lasers and filters
OLT
Rx
DFB Tx
Tx/Rx
Tx/Rx
2E. Coherent receiver and modulator
Logic
AWG
ONU
Rx
Logic
Laser
1:N
OLT
Pol. Div.
Coherent Rx
Modulator
Tx
Tx/Rx
Tx/Rx
AWG
Freq Gen
Logic
Loc Osc
ONU
Logic
Pol. Div.
Coherent Rx
Modulator
Tx
DSP
Control
Loc
Osc
1:N

---
3. [[O-]O]FDM PON
3. [[O-]O]FDM PON
3A. FDM-PON
3C. O-OFDM-PON
3B. OFDM-PON
Lin.
Tx
Lin.
Rx
OLT
10G MAC
Lin. Rx
Lin. Tx
Medium BW ONU
40G MAC
2.5G MAC
Mo-dem
Mo-dem
Mo-dem
10G MAC
Mo-dem
Lin. Rx
Lin. Tx
High BW ONU
2.5G MAC
Mo-dem
Lin. Rx
Lin. Tx
Low BW ONU
2.5G MAC
Mo-dem
RF Frequency
Power
Lin.
Tx
Lin.
Rx
OLT
Bit load
MAC
ONU
IFFT
DAC
Bit un load
FFT
ADC
Lin.
Tx
Lin.
Rx
Bit load
MAC
IFFT
DAC
Bit un load
FFT
ADC
RF Frequency
Power
LO
Bal
Rx
OLT
MAC
+
Serdes
ONU
IFFT
DAC
FFT
ADC
MAC
+
serdes
IFFT
DAC
FFT
ADC
FFT
ADC
IFFT
DAC
Bal
Rx
Mod
Pol
FFT
ADC
IFFT
DAC
Bal
Rx
Bal
Rx
Pol
LO
Mod

---
4. TWDM PON (XG-PON2)
4. TWDM PON	(XG-PON2)
XG-PON2 OLT
BM Rx 1
BM Rx 2
…
BM Rx 8
Tx λ1
Tx λ2
…
Tx λ8
GPON OLT
GPON ONU
RF Overlay
Key Features:
Builds on XG-PON1
Uses splitter based PON
Advantages
Reasonable costs
Up to 80 Gbps
Coexists with deployed GPON
Challenges
Tunable Receivers and Transmitters at ONU
Spectrum allocation
Logic
XGPON2 ONU 1.1
Logic
Laser
Rx
AWG
AWG
WDM1
1:N
XGPON2 ONU 2.1
Logic
Laser
Rx
XGPON2 ONU 8.1
Logic
Laser
Rx

---
NG-PON2 architecture scorecard
NG-PON2 architecture scorecard
TWDM
ALU, BL, CX, HW, MIT, OKI, PMC, ZTE
OFDM-PON
Fuji, ITRI, Hisense, NeoP, Vit, ZTE
IL-WPON
LG-E, ETRI
40G Serial
ALU
RU-WPON
ERIC
[WDM]-[O]-OFDM-PON
NEC
SS-WPON
ALU, HW
Tun-WPON
ADVA
[O]-OFDM-PON
ALU
UD-WPON
NSN
Green = Selected!
Yellow = Optional enhancement
Red means not this time

---
Approved TWDM system  requirements
Approved TWDM system
requirements
Base system: 40G downstream, 10G upstream
  - 4 channels in each direction
  - Compatible with G-PON, XG-PON, and RF video overlay
  - 20km @ 1:64 split ratio fully passive plant capable
Optional extra capabilities
  - 8 channels in each direction
  - 10G upstream
  - DWDM overlay
Standardization is expected to complete July 2013

---
NG-PON2 spectrum (rough consensus)
NG-PON2 spectrum
(rough consensus)
10nm
XG-PON
upstream
G-PON
upstream
1260
1270
1280
1290
1300
1310
1320
1330
1340
1350
1360
NG2
NG2
NG2
NG2
NG2
NG2
NG2
NG2
NG2
NG2
NG2
NG2
NG2
NG2
NG2
NG2
1530
1531
1532
1533
1534
1535
1536
1600
1601
1602
1603
1604
1605
1606
G-PON
downstream
NG2
Video
XG
NG2
1480
1490
1500
1510
1520
1530
1540
1550
1560
1570
1580
1590
1600
1610

---
TWDM standards arrangement
TWDM standards arrangement
G.ngpon2.1 = Requirements
  - Consented at Sep 2012 meeting
G.ngpon2.2 = Physical medium dependent layer
  - Draft in progress
G.ngpon2.3 = TC layer
  - NG-PON2 specific TC features
G.987.3 = Transmission convergence layer
  - 10G upstream to be added to this base standard
G.multi = Wavelength control layer
  - Draft already started in Q2/15
G.988 = ONU management and control interface
  - Standard in force, can be easily reused for TWDM

---
Other topics
Other topics
G.epon
  - Applies OMCI (G.988) to EPON
  - Relevant to P1904.1 Package B systems
G.multi
  - Describes generic multi-wavelength control in PON access systems
G.poc
  - Study of integrated PON-G.fast systems
  - Objective of reducing DP complexity

---
PowerPoint Presentation
Thank you